## Slide 1
01
Audio Recording & Playback
Build the foundation — record 3 seconds of audio and play it back
Raspberry Pi Voice Assistant

## Slide 2
What You'll Learn
Audio Input/Output
Record from a microphone and play back through speakers using sounddevice
Audio Formats
Understand sample rates (16 kHz), bit depth (int16), and mono vs. stereo channels
Python Audio Libraries
Work with sounddevice for I/O and numpy to represent audio as arrays of numbers
Basic Error Handling
Gracefully handle missing or unavailable audio devices
Audio Processing Pipeline
Build the foundation that every later module will depend on

## Slide 3
Key Concepts: Sampling & Data
Audio Sampling (16 kHz)
16,000 measurements per second — enough to capture all human speech frequencies up to 8 kHz
Data Type: int16
Each sample is a 16-bit integer (−32,768 to +32,767), giving 96 dB of dynamic range
Mono Channel
Single-channel audio halves the data vs. stereo and works better for speech recognition
numpy Array
Audio data is represented as a flat numpy array — easy to slice, manipulate, and pass between functions
audio.py constants
SAMPLERATE = 16000 # 16 kHz
DURATION = 3 # seconds
CHANNELS = 1 # mono
DTYPE = np.int16
# Total frames = rate × duration
FRAMES = SAMPLERATE * DURATION
# → 48,000 samples captured

## Slide 4
How It Works
Step 1 — Open Stream
sd.InputStream() opens the microphone; analog sound → digital samples
Step 2 — Read Frames
stream.read(FRAMES) blocks until all frames are captured
Step 3 — Convert
np.frombuffer() turns raw bytes into a numpy array
Step 4 — Play Back
sd.play(audio, SAMPLERATE) sends the array back to the sound card
Step 5 — Wait
sd.wait() blocks until playback finishes before the script exits
Recording snippet
with sd.InputStream(
samplerate=SAMPLERATE,
channels=1,
dtype=np.int16) as stream:
data, _ = stream.read(FRAMES)
audio = np.frombuffer(
data, dtype=np.int16)
sd.play(audio, SAMPLERATE)
sd.wait()

## Slide 5
Stretch Challenges
Change the duration
Edit DURATION = 3 in main.py. What's the shortest recording that still sounds complete?
Change the sample rate
Try SAMPLERATE = 8000 or 44100. Notice quality vs. file size trade-offs.
Quiet it down
Multiply audio by 0.5 before playback. What does that do to volume?
Count your samples
Print len(audio) after recording. Does it equal SAMPLERATE × DURATION?

## Slide 6
Learning Check
Before moving on, you should be able to:
✓ Record audio from your microphone
✓ Play back recorded audio through speakers
✓ Explain what sample rate and bit depth mean
✓ Describe the basic audio recording/playback pipeline
✓ Troubleshoot common audio device issues
Raspberry Pi Voice Assistant · Module complete

## Slide 7
What's Next?
1
Module 2 — Voice Activity Detection
Listen continuously and only capture audio when someone speaks
2
Module 3 — Speech-to-Text
Send captured audio to OpenAI Whisper and get back a transcription
3
Module 4 — AI Chat Response
Pass transcriptions to ChatGPT and display an intelligent reply